!datastate             ( n -- )                           <run>         run.fth
    store datastate for current buffer 

".r                    ( pstr width -- )                  <misc>       misc.fth
    print packed string right justified in width 

"=                     ( pstr1 pstr2 -- flag )            <gen>    genwords.fth
    True if the packed strings are equal. 

"=n                    ( str1 str2 n -- flag )            <gen>    genwords.fth
    True if 1st n bytes of both strings are =. 

"?                     ( pstr1 pstr2 -- flag )            <gen>    genwords.fth
    flag is < 0 if str1 < str2. 
    flag is = 0 if str1 = str2.
    flag is > 0 if str1 > str2.

"?n                    ( str1 str2 n -- flag )            <gen>    genwords.fth
    Compare 1st n bytes of both strings. 
    flag is < 0 if str1 < str2.
    flag is = 0 if str1 = str2.
    flag is > 0 if str1 > str2.

"@f  <dsp>             debug.fth
    
"ad0.name              ( pstr -- )                        <run>         run.fth
    Enter name for a/d 0 * 

"ad1.name              ( pstr -- )                        <run>         run.fth
    Enter name for a/d 1 * 

"ad2.name              ( pstr -- )                        <run>         run.fth
    Enter name for a/d 2 * 

"ad3.name              ( pstr -- )                        <run>         run.fth
    Enter name for a/d 3 * 

"badpix                ( pstr -- )                        <det>         det.fth
    store badpix name * 

"clockpgm              ( pstr -- )                        <det>         det.fth
    store clockpgm name & load it SFX * 

"datapgm               ( pstr -- )                        <det>         det.fth
    store datapgm name & load it SFX * 

"detname               ( pstr -- )                        <det>         det.fth
    store detname * 

"filter                ( pstr -- )                        <run>         run.fth
    Store name of filter * 
    NOTE: does not move to the filter
    use filter name to do that

"fwn                   ( pstr -- )                        <run>         run.fth
    Enter filterwheel name * 
    "BUG" this should load the filter wheel *

"help                  ( pstr -- )                        <tools>     tools.fth
    Get info about word from whatsup.doc file * 

"loaddet               ( pstr -- )                        <det>         det.fth
    load detector data from file. not during crun SFX * 
    NOTE: Parameter order here must match
    the order in savedet

"loaduser              ( pstr -- )                        <xdir>       xdir.fth
    Load user's custom file (pstr) SFX * 

"makedir               ( pstr -- )                        <xdir>       xdir.fth
    Make directory with error checking SFX 

"night                 ( pstr -- )                        <xdir>       xdir.fth
    makes new night directory SFX * 

"object                ( pstr -- )                        <xdir>       xdir.fth
    make new objdir & start sequencing data files SFX * 

"observer              ( pstr -- )                        <run>         run.fth
    Enter observer initials * 

"savedet               ( pstr -- )                        <det>         det.fth
    saves detector as named SFX * 

"savesetup             ( pstr -- )                        <run>         run.fth
    Save run parameters to file SFX * 
    PNOTE: Parameter order here must match *
    the order in "setup *

"seeall                ( pstr -- )                        <tools>     tools.fth
    Show definitions for words of given name * 

"setdatapath           ( pstr -- )                        <xdir>       xdir.fth
    specify new home dir for data SFX * 

"setdir                ( pstr -- )                        <xdir>       xdir.fth
    change directory with error checking SFX 

"setup                 ( pstr -- )                        <run>         run.fth
    load run parameters from file SFX * 
    PNOTE: Parameter order here must match *
    the order in "savesetup *

"siftdsp               ( pstr -- )                        <tools>     tools.fth
    Sift through words in <dsp> for pstr. 

"space                 ( addr -- )                        <dsp>       tools.fth
    Add a space to the end of a string. ** 

"telescope             ( pstr -- )                        <run>         run.fth
    Enter telescope name * 

"vf-active             ( pstr -- )                        <vf>           vf.fth
    Set the active canvas. 

"vf-buffer             ( pstr -- )                        <vf>           vf.fth
    Set the buffer for the active canvas. 

"vf-dofile             ( pstr -- )                        <vf>           vf.fth
    Set the VF macros path to pstr. 

"vf-math               ( mathstr -- )                     <vf>           vf.fth
    Perform simple math in VF. 
    mathstr should look like:
    b#=b#' {*|/|+|-} {b#''|num}

"vf-path               ( pstr -- )                        <vf>           vf.fth
    Set the datapath for VF to pstr. 

"vfcmd                 ( pstr -- )                        <dsp>          vf.fth
    Use to create commands in FORTH files. 
    Stores pstr in vfstring and runs
    send-to-vf. Example:
    p" active e" "vfcmd

"vocsifting            ( pstr -- )                        <tools>     tools.fth
    List all words containing pattern in pstr * 

"whatvoc               ( pstr -- )                        <tools>     tools.fth
    List all words with the given name in pstr * 

#>pstr                 ( n1 pstr -- )                     <dsp>       tools.fth
    Convert a number into a packed string. ** 

#steps                 ( -- n )                           <urfp>       urfp.fth
    Calculate the number of clock pulses required 
    to adjust the DAC voltage on circuit 2 or 3.

$+l  <dsp>             debug.fth
    
("makedir)             ( pstr -- errorcode )              <xdir>       xdir.fth
    Make directory SFX 

("setdir)              ( pstr -- errorcode )              <xdir>       xdir.fth
    change directory SFX 

()dim                  ( n -- )                           <gen>    genwords.fth
    create an n dimensional array. Assumes 4 bytes / integer. 
    SHOULD use /n instead of 4; /n* instead of 4 *

(.name)                ( pstr -- )                        <xdir>       xdir.fth
    display pstr or "none" if empty 

(body)  <dsp>          debug.fth
    
(checkrunmode)         ( -- )                             <runrun>   runrun.fth
    abort with message if in CRUN mode 
    some variables must NOT change when in CRUN mode
    words that change them call checkrunmode First

(cook)                 ( -- )                             <con>     console.fth
    line buffered input SFX * 

(dbugstatus
    
(eol)                  ( addr -- )                        <misc>       misc.fth
    Store rest of line as a 72 char string at addr. 

(eol>pstr)             ( addr -- )                        <misc>       misc.fth
    Store rest of line as a packed string. 

(fitsheader)           ( fid -- fid )                     <fits>       fits.fth
    Write FITS header via writeline SFX 
    to output specified by writeline
    BUG: BSCALE & BZERO are wrong, must
    be corrected for spectrum a/d
    NOTE: our comments are not written
    like standard FITS parameters
    They are written as FITS comments,
    & include the comment name & data
    SHOULD: keep track of # of header
    lines then fill to end of block
    with HISTORY ... HISTORY END
    see fitstail for pixel analogue
    SHOULD: provide interface for CUSTOM
    ie: 10 objects CUSTOM0 ... CUSTOM9
    each a line. CUSTOM software
    dumps lines into these variables,
    (fitsheader) writes these 10 to
    the FITS file.

(fp)                   ( itime -- \squareside lr ll ctr u <nasm>         fp.fth
    Get ave intensity of 
    5 different detector locations.
    This is the only command to be used during
    calibration mode!
    Sets the integration time, takes a src and bkg
    frame, then subtracts them. 5 fpsquare commands
    are then executed that return the avg intensity
    of each square. The results are then printed
    to the screen, with the proper formatting,
    so that the NASM computer can acquire them.

(fptweak)              ( n -- )                           <urfp>       urfp.fth
    Set the voltage on DAC n. 

(gc)                   ( addr -- )                        <run>         run.fth
    Store rest-of-line as a 72 char comment at addr 

(listtype)             ( acf -- )                         <tools>     tools.fth
    List words defined by the word with this acf * 

(loaddata)             ( addr count -- addr count )       <runrun>   runrun.fth
    Copy to parameter block SFX 

(loaddsp)              ( pstr -- )                        <dspif>       dsp.fth
    Load NIR program onto dsp board & SFX ** 
    run its setup subprogram SFX **

(nasm-display)         ( \squareside F: lr ll ctr ur ul - <nasm>         fp.fth
    Display 5 box 
    intensities for NASM software to grab.
    format the output and display it

(nir-display)          ( \squareside F: lr ll ctr ur ul - <nasm>         fp.fth
    Write 5 box intensities 
    to a file (z-i.dat) for later processing.
    z is AD0, y is AD2, x is AD3 in adu units.

(nm)                   ( lambda[nm] -- )                  <fil>    ./fwheels/fi
    move to lambda SFX * 

(open-read)            ( pstr -- fid | 0 )                <misc>       misc.fth
    Open file for reading SFX 

(open-write)           ( pstr - fid | 0 )                 <misc>       misc.fth
    Open file for writing SFX 

(printline)            ( -- )                             <fits>       fits.fth
    Display line on screen. 

(raw)                  ( -- )                             <con>     console.fth
    key buffered input (single key)-see man on stty SFX * 

(readarray)            ( -- )                             <partial> partial.fth
    read array, mode stored in runflag SFX * 

(sampconst)            ( n "name" -- )                    <run>         run.fth
    Create a sampling mode word SFX * 
    # must agree with dsp 56001 programs *
    PNOTE: should be named sampmode: *
    PNOTE: does> should also copy *
    sampmode name to a variable, *
    like filter (see filterI.fth) *

(savea-)               ( -- )                             <fits>       fits.fth
    After executing an a-, save sigbuf to disk 
    in a file called "aminus". This is similar
    to how sscan and bscan save their buffers
    (i.e. savetmp).

(savedata)             ( -- )                             <fits>       fits.fth
    Save object datafile, pixels in fitspixbuf SFX * 
    SHOULD: avoid duplicating code in savedata & savetmp *
    by putting common code in a new word *
    & having them put params on stack & call it *

(savedet)              ( -- )                             <run>         run.fth
    Ask user to save or not to save changed det parameters. 

(savereturn)           ( -- )                             <nod>         nod.fth
    Save parameters before executing a fast, * 
    moderate or slow command.

(savetmp)              ( -- )                             <fits>       fits.fth
    like savedata but saves to a fixed temporary file SFX * 
    SHOULD: avoid duplicating code in savedata & savetmp *
    by putting common code in a new word *
    & having them put params on stack & call it *

(setdac)               ( n dac# -- )                      <det>         det.fth
    Fake DT version of set d/a convert 

(showrun)              ( -- )                             <run>         run.fth
    Display non-det parameters 

(sstatus
    
(writeline)            ( fid -- fid )                     <fits>       fits.fth
    Write line to file SFX 

*lv  <dsp>             debug.fth
    
+fitslength            ( n -- n )                         <fits>       fits.fth
    # of bytes in the complete fits file * 

+res                   ( -- )                             <fil>    ./fwheels/fi
    move to lambda = (lambda+[lambda/res]) w/backlash SFX * 

+slash                 ( pstr -- pstr )                   <misc>       misc.fth
    Add / at end if absent 

->fwp                  ( lambda[nm] -- fwp )              <fil>    ./fwheels/fi
    Convert wavelength -> position 

->fwp.l''              ( offset -- fwp )                  <fil>    ./fwheels/fi
    calculate fwp from offset to l'' 

->nm                   ( fwp -- lambda[nm] )              <fil>    ./fwheels/fi
    Convert position -> wavelength 

-ext                   ( pstr -- pstr' )                  <misc>       misc.fth
    removes .EXT from file name 

-path                  ( pstr -- pstr )                   <misc>       misc.fth
    strips path information from pstr 

-res                   ( -- )                             <fil>    ./fwheels/fi
    move to lambda = (lambda-[lambda/res]) SFX * 

-slash                 ( pstr -- pstr )                   <misc>       misc.fth
    Remove / from end if present 

.1d                    ( n field_len -- )                 <gen>    genwords.fth
    Right justified print for signed * 
    number, 1 digit to right of decimal *

.1mvolts>a/d           ( mV*10 -- a/d-counts              <dt>       dt2823.fth
    Converts mv*10 to a/d data ** 
    by dividing the mv*10 by 3.0518. Uses 16 bit A/D,
    32 bit normals.

.clockpath             ( -- )                             <xdir>       xdir.fth
    display clockpath 

.console               ( n -- )                           <con>     console.fth
    type number without trailing space 

.dataacqpath           ( -- )                             <xdir>       xdir.fth
    display dataacqpath 

.datapath              ( -- )                             <xdir>       xdir.fth
    display datapath 

.datastate             ( n -- )                           <run>         run.fth
    display data state 

.detpath               ( -- )                             <xdir>       xdir.fth
    display detpath 

.errmsg                ( n -- )                           <runrun>   runrun.fth
    print error message number n 

.field                 ( addr -- )                        <run>         run.fth
    Display a string right justified in 9 chars 
    NOTE: assumes string size = 8

.file                  ( -- )                             <xdir>       xdir.fth
    display current object file w/ path 

.filename              ( -- )                             <xdir>       xdir.fth
    display object name w/o path 

.fitsheader            ( -- )                             <fits>       fits.fth
    write fits header to screen SFX * 

.gap                   ( -- )                             <run>         run.fth
    insert 15 spaces 

.label                 ( pstr -- )                        <run>         run.fth
    Display pstr left justified in 16 chars; + ":" 

.ncol                  ( -- )                             <partial> partial.fth
    print value of ncol 

.night                 ( -- )                             <xdir>       xdir.fth
    display current night path 

.nightname             ( -- )                             <xdir>       xdir.fth
    display night name w/o path 

.nimage                ( -- )                             <dsp>      runrun.fth
    Display the current number of images to to be saved 
    into one FITS file.

.nimagemax             ( -- )                             <dsp>      runrun.fth
    Display the maximum number images that can be 
    handled by sigbuf or bkgbuf.

.nrow                  ( -- )                             <partial> partial.fth
    print value of nrow 

.num                   ( addr -- )                        <run>         run.fth
    Display int right justified in 9 chars 

.object                ( -- )                             <xdir>       xdir.fth
    display current object path w/ path 

.p1row                 ( -- )                             <partial> partial.fth
    print value of p1row 

.paths                 ( -- )                             <xdir>       xdir.fth
    Show all file paths that have been set. 

.pcount                ( -- )                             <partial> partial.fth
    print value of pcount 

.pnrow                 ( -- )                             <partial> partial.fth
    print value of pnrow 

.primname              ( prim# -- )
    
.samptype              ( n -- )                           <run>         run.fth
    display word name for sampmode n 

.sr  <dsp>             debug.fth
    
.tmps                  ( -- )                             <dsp>       tmptr.fth
    prints out voltage and temp for dro,fo,ws ** 

.userfile              ( -- )                             <dsp>        xdir.fth
    Print last custom user file loaded. * 

0>dup                  ( n -- n,n/n )                     <dsp>       debug.fth
    DUP if n>0. 

0set                   ( addr -- )                        <gen>    genwords.fth
    Store 0 at the address. (See false! below.) 

16buf                  ( -- )                             <dsp>      runrun.fth
    Use rdblock16buf to get data from Spectrum boards SFX ** 

16i                    ( -- )                             <dsp>      runrun.fth
    Use rdblock16i to get data from Spectrum boards SFX ** 
    SHOULD: use get16i. It uses the old get.data instead.

1d                     ( n -- pad_address #_characters )  <gen>    genwords.fth
    create ascii string of * 
    signed #, xxxx.y *

1set                   ( addr -- )                        <gen>    genwords.fth
    Store 1 at the address. (See true! below.) 

1sp                    ( n -- )                           <dsp>    ./fwheels/fi
    take data at n wavelengths using +res SFX ** 

2**n                   ( n -- 2^n )                       <gen>    genwords.fth
    returns 2 to the nth power if n>=0. Else 1. 

2sp                    ( n -- )                           <dsp>    ./fwheels/fi
    same as 1sp, but do 2 scans/wavelength SFX ** 

2sr                    ( -- )                             <dsp>         nod.fth
    take 2 source runs & nod the telescope SFX ** 

3dup                   ( n1 n2 n3 -- n1 n2 n3 n1 n2 n3 )  <gen>    genwords.fth
    Copy 3 elements on top of stack. 

>bak                   ( pstr -- pstr' )                  <misc>       misc.fth
    changes file extension to .BAK 

>boolean               ( n -- f )                         <misc>       misc.fth
    convert number to boolean 

>fn                    ( file-pstr dir-pstr -- fullname ) <xdir>       xdir.fth
    cat filename to end of dir string 

>lower                 ( addr count -- )                  <misc>       misc.fth
    convert text to lower case 

>nst  <dsp>            debug.fth
    
>signed                ( n1 -- n2 )                       <gen>    genwords.fth
    Sign extends a 16-bit number to 32-bits. 

>upper                 ( addr count -- )                  <misc>       misc.fth
    convert text to upper case 

?#                     ( n -- )                           <gen>    genwords.fth
    Aborts if n>num of stack elements under n 

?enough                ( 1 -- )                           <dsp>       debug.fth
    Are there enough stack parameters for the next word 
    to execute?

?fileexists            ( pstr -- flag )                   <misc>       misc.fth
    Checks for existence of file (pstr) SFX * 

?key                   ( -- char or 0 )                   <con>     console.fth
    If key hit, then return the value of SFX 
    key, else 0

?log2                  ( n -- 1|log2[n] )
    
@@
    
@datastate             ( -- n )                           <run>         run.fth
    return datastate of current buffer 

@nimage                ( -- n )
    
@nimage.max            ( -- n )                           <runrun>   runrun.fth
    Return max number of images that can be 
    stored in sigbuf/bkgbuf based upon
    nrow and ncol.

@t@
    
@w@
    
a-                     ( -- )                             <dsp>    imagproc.fth
    subtract pixels in bkgbuf from pixels in sigbuf SFX ** 
    store result in bkgbuf

a-.store.hist          ( -- )                             <proc>   imagproc.fth
    store "a-" and file names in hist * 

a/d.allow.set.channel  ( -- )                             <dt>       dt2823.fth
    3. Load CHANCSR SFX 

a/d.channel.is.set     ( -- )                             <dt>       dt2823.fth
    5. Disable further writes to SFX 
    RAM-channel etc., enable next stuff

a/d.diff               ( a b -- n )                       <urfp>       urfp.fth
    For a/d boards a and b, calculate a-b in .1mV. 

a/d.get.data           ( -- n )                           <dt>       dt2823.fth
    9. Read data from ADDAT register. SFX 
    ADDAT holds a 16-bit Two's Complement
    Number. Bits 16-31 are 0. For 32-bit
    CFORTH this number must be sign-extended.
    If bit 15 is 0, the number is already
    sign extended: Bits 16-31 are 0.
    If bit 15 is 1, bits 15-31 must be set to 1.
    This can be done in hex by (ffff not or),
    or by subtracting 10000.

a/d.init               ( -- )                             <dt>       dt2823.fth
    2. Load SUPCSR SFX 

a/d.set.channel        ( n -- )                           <dt>       dt2823.fth
    4. Load ADCSR SFX 

a/d.set.clock          ( -- )                             <dt>       dt2823.fth
    1. Set clock to 100 KHz. SFX 

a/d.set.multiplex      ( -- )                             <dt>       dt2823.fth
    6. Load SUPCSR 

a/d.trigger            ( -- )                             <dt>       dt2823.fth
    7. Wait for MUXBUSY to clear, load SUPCSR SFX 

a/d.wait.for.a/d.done  ( -- )                             <dt>       dt2823.fth
    8. Wait for A/DDONE set. SFX 

a/d>.1mvolts           ( a/d-counts -- mV*10 )            <dt>       dt2823.fth
    converts a/d data to mVx10 ** 
    by multiplying the a/d counts by 3.0518
    ( =100,000/32,768 ). Uses 16 bit A/D, 32 bit normals.

a/d>kelvin             ( ' \ADx -- temp|flag )            <xshow>  xshowall.fth
    Similar to match.tmps but doesn't 
    print the temps to the screen.

abort.run              ( -- )                             <runrun>   runrun.fth
    Stop all boards and check error codes SFX 

ad0name                ( "name" -- )                      <dsp>         run.fth
    Enter name for ad0 ** 

ad1name                ( "name" -- )                      <dsp>         run.fth
    Enter name for ad1 ** 

ad2name                ( "name" -- )                      <dsp>         run.fth
    Enter name for ad2 ** 

ad3name                ( "name" -- )                      <dsp>         run.fth
    Enter name for ad3 ** 

adctime                ( n -- )                           <dsp>         run.fth
    Set A/D convert time (units: 0.1 usec) ** 
    NOTE: can't change during crun

advance.to.free.objnum ( -- )                             <xdir>       xdir.fth
    When creating an object, advance SFX * 
    the objfile to an objnum that does
    not already exist on the disk.
    This prevents you from overwriting
    existing data when return to a
    previously used object name.

advance_fb             ( -- )                             <vf>           vf.fth
    Advance VF filebuffer to next in line. 

aliases                ( -- )                             <tools>     tools.fth
    List all aliased words in the dictionary ** 

allnames               ( -- )                             <dsp>       tools.fth
    Print alphabetical listing of all words. 

allwords               ( -- )                             <dsp>       tools.fth
    List all words in the dictionary, by vocabulary ** 

aname                  ( "char" -- )                      <dsp>       tools.fth
    List all words beginning with char. 

ansi                   ( -- )                             <con>     console.fth
    output ANSI header: <esc>[ 

assertflag             ( -- )                             <dspif>       dsp.fth
    Raise flag that dsp board reads. SFX * 

ave                    ( col row -- )                     <red>         red.fth
    average pixval for user rectangle. Will be clipped 

ave.rect               (F: -- ave )                       <red>         red.fth
    average pixval for clipped rectangle on Float Stack 

backlash               ( -- )                             <dsp>       wheel.fth
    perform backlash movement on the filterwheel SFX ** 

badpix                 ( "name" -- )                      <dsp>         det.fth
    store badpix filename ** 

bankbuf                ( boardnum memtype -- pcbuf )      <runrun>   runrun.fth
    Get det output buffer addr SFX * 

banner                 ( -- )                             <run>         run.fth
    Draw a line 80 characters long 

bell                   ( -- )                             <misc>       misc.fth
    That for which the bell tolls. 

bgsub                  ( -- )                             <dsp>          vf.fth
    Toggle bkg subraction from src frames on/off. ** 

bit-off                ( n -- )                           <fil>       wheel.fth
    set the nth bit of outword and port to 0. SFX * 

bit-on                 ( n -- )                           <fil>       wheel.fth
    set the nth bit of outword and port to 1. SFX * 

bkg                    ( -- )                             <dsp>         run.fth
    Make bkg buffer the current image buffer SFX ** 

bkg.params             ( -- )                             <run>         run.fth
    select bkg file & history SFX 

blank                  ( addr n -- )                      <misc>       misc.fth
    fills with blanks 

bmax                   ( n -- )                           <dsp>          vf.fth
    Set the maximum number of file buffers to use in VF 
    and reset vf.srcfb to 0.

boardnum               ( -- )                             <dsp>      runrun.fth
    buffer containing # of each Spectrum board used ** 
    SHOULD: not be a user word - use cb db1 db2 **

body  <dsp>            debug.fth                         in body, f
    
br                     ( -- )                             <dsp>         nod.fth
    do a brun & nod the telescope SFX ** 

brun                   ( -- )                             <dsp>      runrun.fth
    Select bkg buffer, then execute run SFX ** 

bscan                  ( -- )                             <dsp>      runrun.fth
    Select bkg buffer, then execute scan SFX ** 

burst                  ( -- )                             <dsp>      runrun.fth
    Clock array;throw away frames as fast as possible SFX ** 

burstread              ( -- )                             <partial> partial.fth
    read array in burst mode SFX * 

bytes/buffer           ( -- n )                           <partial> partial.fth
    returns bytes/buffer 

calculate.loops/msec   ( -- )                             <fil>       wheel.fth
    Calculate the number of loops a do SFX * 
    loop requires to loop 1 msec.

call                   ( offset hostadr adr1 len1 -- )    <rpc>         rpc.fth
    Send a string to host via RPC. ** 

cat.float.value        (F: f1 -- )                        <xshow>  xshowall.fth
    Add " `float'" to xsstring. 

cat.number.value       ( n1 -- )                          <xshow>  xshowall.fth
    Add " `integer'" to xsstring. 
    n1 is a number

cat.string.value       ( pstr -- )                        <xshow>  xshowall.fth
    Add " `pstr'" to xsstring. 

cb                     ( n -- )                           <dsp>      runrun.fth
    n=Spectrum Board to use for clocking the array ** 

cd'                    ( -- )                             <dsp>    ./fwheels/fi
    bump filter wheel to halfway between filters,= cd SFX ** 

cencol                 (F: -- centroid_col )              <red>         red.fth
    col for centroid of stats area on Float Stack 

cenrow                 (F: -- centroid_row )              <red>         red.fth
    row for centroid of stats area on Float Stack 

check.col.limit        ( n -- n|abort )                   <det>         det.fth
    ncol must be divisible by 8! 

check.row.limit        ( n -- n|abort )                   <det>         det.fth
    nrow must be divisible by 2! 

checkdsps              ( -- rf ef )                       <dsp>      runrun.fth
    rf = t if ALL boards stopped SFX 
    ef = t if ANY errors

ci                     ( -- char )                        <con>     console.fth
    inputs char w/o screen echo - NOPE!! SFX 

clear-linecount
    
clear.buffer           ( -- )                             <partial> partial.fth
    set all pixels to 0 in current buffer 

clear.filename         ( -- )                             <run>         run.fth
    Clear current buffer's filename 

clear.hist             ( -- )                             <run>         run.fth
    clear the history buffer 

clear.string           ( pstr -- )                        <misc>       misc.fth
    Clear the contents of the specified pstr. 

cleardata              ( -- )                             <dsp>     partial.fth
    clear current image buffer of data SFX ** 

clip.col               ( col -- )                         <red>         red.fth
    Determine min/max col in stats area 

clip.rect              ( col row -- )                     <red>         red.fth
    Determine stats area given user col & row 

clip.row               ( row -- )                         <red>         red.fth
    Determine min/max row in stats area 

clockboard             ( -- )                             <dspif>       dsp.fth
    selects clock board 

clockpgm               ( "name" -- )                      <dsp>         det.fth
    store clockpgm filename & load it SFX ** 

close-scandir
    
cls                    ( -- )                             <con>     console.fth
    home cursor, clear screen 

cname  <tools>         tools.fth
    
co                     ( char -- )                        <con>     console.fth
    replace old DOS call with ordinary emit 

col                    ( col -- )                         <dsp>         red.fth
    Column statistics and display ** 

col>adr                ( col -- line.addr maxwid )
    
col>adr-180            ( col -- line.addr maxwid )
    
colons                 ( -- )                             <tools>     tools.fth
    List all colon defined words in the dict ** 

comment                ( -- )                             <fits>       fits.fth
    set keyword = COMMENT 

comment0               ( "string" -- )                    <dsp>         run.fth
    Create comment 0 called "string". ** 
    Create a word called "string" that acts
    like a global comment and store the
    address of the comment text at adr.

comment0default        ( -- )                             <run>         run.fth
    Make comment0 be nasmfpc by default 
    and comment0name NASMFPC by default.

comment1               ( "string" -- )                    <dsp>         run.fth
    Create comment 1 called "string". ** 
    Create a word called "string" that acts
    like a global comment and store the
    address of the comment text at adr.

comment2               ( "string" -- )                    <dsp>         run.fth
    Create comment 2 called "string". ** 
    Create a word called "string" that acts
    like a global comment and store the
    address of the comment text at adr.

comment_clean
    
comments               ( -- )                             <dsp>         run.fth
    Display comment fields. 

cons                   ( -- )                             <tools>     tools.fth
    List all constants in the dictionary ** 

cook                   ( -- )                             <con>     console.fth
    Puts terminal in cook mode, restore tty settings SFX 

corrupt.hist           ( -- )                             <run>         run.fth
    Use before starting to copy pix to databuffer 
    get data sets hist to this, gets data, then
    calls raw hist if this is left in history then
    raw hist wasn't called so get data must have
    failed/been interrupted.

cr.wait                ( -- )                             <partial> partial.fth
    wait for <cr> SFX 

crtox
    
crun                   ( -- )                             <dsp>      runrun.fth
    Clock array continuously, same time/all frames SFX ** 
    crun exists to achieve stability in detector. **
    NOTE: Throw away frames & coadd frames **
    take the same amount of time **

crunread               ( -- )                             <partial> partial.fth
    read array in crun mode SFX * 

cstr>pstr              ( cstr -- )                        <misc>       misc.fth
    Convert a cstr to a pstr 

cstrlen                ( cstr -- n )                      <misc>       misc.fth
    Place length of non-packed string on stack. 

ctr                    ( -- )                             <dsp>         nod.fth
    inspect the central region of the array ** 

ctstime                ( n -- )                           <dsp>         run.fth
    Set clamp to sample time (units: 0.1 usec) ** 
    NOTE: can't change during crun

cvf                    ( fwp nm -- )                      <fil>    ./fwheels/fi
    Init cvf. 

d"@  <dsp>             debug.fth
    
d/a.channel            ( n -- )                           <dt>       dt2823.fth
    2. Select channel n (0 or 1) for DAC output SFX 

d/a.init               ( -- )                             <dt>       dt2823.fth
    1. Initialize the D/A SFX 

d/a.send.data          ( -- )                             <dt>       dt2823.fth
    4. Set SUPCSR to output what is in DADAT. SFX 

d/a.set.data           ( n -- )                           <dt>       dt2823.fth
    3. Put value in D/A Data Register. SFX 
    Clip [-32768, 32767]

dac.high               ( mV -- )                          <dsp>        urfp.fth
    Set the high value for the FP DAC in mV. 

dac.low                ( mV -- )                          <dsp>        urfp.fth
    Set the low value for the FP DAC in mV. 

dash                   ( addr len -- )                    <scandir> scandir.fth
    Fill a line with "-". 

databoard              ( n -- )                           <dspif>       dsp.fth
    selects data board n 1..7 (nir use sequence #s) 

databuffer             ( -- addr )                        <dsp>         run.fth
    Address of current image buffer. ** 
    SHOULD: be set by src and bkg

datadsps               ( -- lastdsp+1 1 )                 <det>         det.fth
    returns indices for do-loops on databoards 

datapgm                ( "name" -- )                      <dsp>         det.fth
    store datapgm filename & load it SFX ** 

datatcolon?  <dsp>     debug.fth
    
datatdoes?  <dsp>      debug.fth
    
datcolon?  <dsp>       debug.fth
    
datdoes?  <dsp>        debug.fth
    
db1                    ( n -- )                           <dsp>      runrun.fth
    n=Spectrum Board to use for 1st-2nd detector outputs ** 

db2                    ( n -- )                           <dsp>      runrun.fth
    n=Spectrum Board to use for 3rd-4th detector outputs ** 

dbdic  <dsp>           debug.fth
    
dbi!  <dsp>            debug.fth
    
dbj!  <dsp>            debug.fth
    
dbl!  <dsp>            debug.fth
    
dc                     ( -- )                             <dsp>       extra.fth
    Look at a charge dump for dark current, etc. SFX ** 

debug2                 ( "word" -- )                      <dsp>       debug.fth
    debug <word> , Then space-bar single-steps ** 
    through <word>.

defs                   ( -- )                             <tools>     tools.fth
    List all deferred words in the dictionary ** 

detname                ( "name" -- )                      <dsp>         det.fth
    store det filename ** 

dic@
    
dicsearch              ( -- )                             <tools>     tools.fth
    Loop through all vocabs in dictionary, call vocsearch 

dict
    
dirtydet               ( -- )                             <det>         det.fth
    detector variables have changed since last loaddet/savedet 

display                ( -- )                             <dsp>          vf.fth
    Toggle auto-display of image data in VF on/off. ** 

dnext  <dsp>           debug.fth
    
do.rect                ( col row -- )                     <red>         red.fth
    Calculate stats for rectangle given col&row * 

down                   ( -- )                             <fil>       wheel.fth
    prepare to go down steps. Set the direction bit to 1. SFX ** 

dsp  <dsp>             debug.fth
    
dspsift                ( "word" -- )                      <dsp>       tools.fth
    Sift only in <dsp> vocabulary. ** 

dt.help                ( -- )                             <dt>       dt2823.fth
    What shared words do ** 

echo-rpc               ( adr len -- )                    reply ;
    
even                   ( n1 -- n2 )                       <dsp>       debug.fth
    Adjusts a number to make it even. n2 >= n1 

exact.time->str        ( hundredths sec min hour -- pstr  <fits>       fits.fth
    Convert 
    exact.time to h:m:s.hs format.

exact.time>msec        ( h s m H -- n )                   <fil>       wheel.fth
    Convert exact.time output into 
    an integer with units of msecs.

extends                ( -- )                             <tools>     tools.fth
    List all C extensions in the dictionary ** 

f#>pstr                (F: fp P: pstr -- )                <dsp>       tools.fth
    Convert a floating pt # to a packed string. ** 

f.sr  <dsp>            debug.fth
    
factor?                ( a b -- flag )                    <partial> partial.fth
    true if a is a factor of b; else false 

false!                 ( addr -- )                        <gen>    genwords.fth
    Stores false at ADDR. Used where DRO used 0set 
    to store FALSE.

fast                   ( -- )                             <dsp>         nod.fth
    go into fastest clocking mode SFX ** 

fastphot               ( -- )                             <dsp>      runrun.fth
    Toggles between fast photometry and 
    normal data acquisition modes.
    When in fast photometry buffer mode, special
    subsets of certain words get executed
    instead of the regular ones.

fbrun                  ( -- )                             <dsp>      runrun.fth
    Select bkg buffer, then execute frun. SFX 

field                  ( offset "base name" -- )          <misc>       misc.fth
    create field offset pointer 

field!                 ( pstr field length -- )           <misc>       misc.fth
    store string in field 

field>scandir          ( addr len -- addr len )           <scandir> scandir.fth
    Leaves address and length 
    of string without whitespace.

field>string           ( field length -- pstr )           <misc>       misc.fth
    convert field to packed string 

filevar:               ( "name" -- )                      <misc>       misc.fth
    Create a file name variable - 80 chars 

filter                 ( wavelength bandwidth fwp-offset  <fil>    ./fwheels/fi
    SFX * 
    -- creates a filter-word. (pfa) has bandwidth, (pfa+4) has
    wavelength, <pfa+8> has offset in fwp from l'. execution of
    filter-word stores filter, wavelength, bandwidth, and filter
    wheel position in header, updates status line, and moves
    filter wheel.

findlast               ( pstr char -- pstr index|0 )      <misc>       misc.fth
    finds last occurence of char 

fitsheader             ( fid -- fid )                     <fits>       fits.fth
    write fits header to data file SFX * 

fitstail               ( fid n -- fid )                   <fits>       fits.fth
    Fill out file to multiple of fitsblksize SFX 

flines                 ( fd len -- n )                    <scandir> scandir.fth
    Return the total number of lines in a file. 
    given the file id and the length of a line.

fo.a/d>temp            ( a/d[fo] -- temp[fo] flag )       <tmp>       tmptr.fth
    Calculate FO temp from A/D * 

fo.correct             ( mV*10 -- mV*10 )                 <tmp>       tmptr.fth
    corrects fo voltage for buffer * 
    amplifier gain and offset

fp                     ( \itime -- )                      <dsp>          fp.fth
    Get 5 box intensities and display them 
    depending on which fp is being used.
    nasm-fp and nir-fp chooses the intensity
    display method.

fp.reset.counter       ( -- )                             <urfp>       urfp.fth
    Cause the counter on the URIR FP to start 
    over at 0.

fp.step                ( -- )                             <urfp>       urfp.fth
    Increase V on DAC by #steps. 

fpbrun                 ( -- )                             <dsp>          fp.fth
    Temporarily use fprun instead of fpnew to save fp 
    calibration data to bkg buffer.

fpbscan                ( -- )                             <dsp>          fp.fth
    SFX ** 

fpcal                  ( Vstart Vend Vstep -- )           <dsp>          fp.fth
    Ramp VGATE from Vstart to Vend by 
    Vstep.

fpnew                  ( -- )                             <dsp>          fp.fth
    Fetch ITIME value and execute fp. 
    NASM uses this in their execute script.

fprun                  ( -- )                             <dsp>          fp.fth
    Save data from fpnew scan and add x,y,z parameters to 
    NASMFPC comment field.

fpscan \               ( -- )                             <nasm>         fp.fth
    Replaces scan for fpsscan and fpbscan. 
    Executes w/o showall and savetmp to increase
    speed.
    Had to include all of the specific code
    so that all comments could be removed!
    This code is intentionally ugly because
    the comments had to be removed!!!!!!!!

fpsquare               ( col row -- F:\ave )              <dsp>          fp.fth
    Computes avg intensity of square with 
    center at (col x row). Similar to
    square except that visual
    representation of square is suppressed.

fpsquares              ( -- )                             <dsp>          fp.fth
    Print out squares for fp folks. 
    Like fp but requires the image to already
    be scanned.

fpsrun                 ( -- )                             <dsp>          fp.fth
    Temporarily use fprun instead of fpnew to save fp 
    calibration data to src buffer.

fpsscan                ( -- )                             <dsp>          fp.fth
    SFX ** 

fptweak                ( mV n -- )                        <dsp>        urfp.fth
    Adjust the voltage on DAC n by mV. SFX ** 

frun                   ( -- )                             <dsp>      runrun.fth
    Get nimage images then save as 1 fits file. SFX 

fscan                  ( -- )                             <dsp>      runrun.fth
    Fast photometry version of scan SFX ** 

fsrun                  ( -- )                             <dsp>      runrun.fth
    Select src buffer, then execute frun. SFX 

ftime                  ( pstr -- )                        <fits>       fits.fth
    Get exact.time and store as time of scan start. 

fvariable              ( "name" -- )                      <red>         red.fth
    create a floating point variable SFX 

fw                     ( n -- )                           <dsp>       wheel.fth
    move to new fwp=n, check bounds & backlash SFX ** 

fw!                    ( n -- )                           <dsp>       wheel.fth
    store new FilterWheel Position (fwp) if in bounds. ** 

fw-init                ( -- )                             <fil>       wheel.fth
    initialize parameters for stepping. SFX ** 

fwmessage              ( -- )                             <fil>       wheel.fth
    Error message for fw not between allowable limits * 

fwn                    ( "name" -- )                      <dsp>         run.fth
    Enter filterwheel name (SFX) ** 
    "BUG" this should load the filter wheel **

fwp                    ( n -- )                           <dsp>         run.fth
    Set filterwheel position ** 

gc                     ( "rest-of-line" -- )              <dsp>         run.fth
    Enter a global comment ** 

gc_clean               ( -- )                             <run>         run.fth
    Erase global comment 

get-request            ( -- false | adr len true )
    
get.a/d                ( n -- v )                         <dt>       dt2823.fth
    Channel n, 0<=n<=3, Gain==1, get A/D SFX ** 
    returns a 32-bit Two's Complement # **
    from -32768 to 32767. **

get.a/d.mv             ( n -- v )                         <dt>       dt2823.fth
    Same as GET.A/D but V is 10ths of millivolts SFX * 

get.all.a/d            ( -- )                             <run>         run.fth
    Get & store current A/D inputs SFX * 

get.cur                ( line col -- )                    <con>     console.fth
    gets current cursor position 

get.data               ( -- )                             <dsp>      runrun.fth
    Move pixels from databoards -> databuffer SFX ** 
    added history manipulation & deferred call

get.error.code         ( -- n )                           <runrun>   runrun.fth
    # of error message returned by dsp program SFX 

get.key                ( -- char )                        <con>     console.fth
    get next key SFX 

get11                  ( start row -- )
    
get16buf               ( -- )                             <runrun>   runrun.fth
    Move pixels from databoards -> databuffer (16buf) SFX * 

get16i                 ( -- )                             <runrun>   runrun.fth
    Move pixels from databoards -> databuffer via 16i SFX * 
    SHOULD: be used by 16i. It isn't

getboard               ( -- board# )                      <dspif>       dsp.fth
    Number of current board (spectrum numbering) 

getbuffer              ( -- addr )                        <dsp>         run.fth
    Address of current image buffer. ** 
    If in fast photometry mode, add
    appropriate imagebuf size.
    SHOULD: be set by src and bkg

getline                ( fid -- fid addr )                <det>         det.fth
    read line from file SFX 
    NOTE: compare w/ version in fits.fth

getnextbp              ( a,top bp#,bottom bp# -- a,next b <tmp>       tmptr.fth
    finds bp# of next * 
    highest data pair above a (a is in acurv)

getnum                 ( fid -- fid num )                 <det>         det.fth
    read number from file SFX 

getpix                 ( col row -- pixval )              <red>         red.fth
    Value of pixel in current buf at col&row ** 

getrundata             ( -- addr #words )                 <runrun>   runrun.fth
    Copy dsp 56001 program parameters to block 
    SHOULD already store params in a block
    like det, so they don't need to be
    copied to pad
    SHOULD create "implicit" variables -
    dsperror ncolread nrowread nshift
    SHOULD do validity check first, not last

gettime                ( -- )                             <misc>       misc.fth
    gets date & time pstrings, depends on extensions 
    thedate = 'dd/mm/yy' (FITS format!!)
    thetime = 'hh:mm:ss' (local machine time)

gitdb,da               ( a,nextbp -- a,b1-b2,a1-a2 )      <tmp>       tmptr.fth
    get db,da of slope of data * 
    pairs surrounding a (a on acurv, b on bcurv

help                   ( "word" -- )                      <dsp>       tools.fth
    Get help about word from whatsup.doc file ** 

help.red               ( -- )                             <dsp>         red.fth
    help for data reduction words ** 

history                ( -- )                             <fits>       fits.fth
    set keyword = HISTORY 

home                   ( -- )                             <con>     console.fth
    homes cursor 

in
    
in.dt.port0            ( -- n )                           <dt>       dt2823.fth
    Sets DIO for Low-Byte In, returns Low-Byte SFX * 

in.dt.port1            ( -- n )                           <dt>       dt2823.fth
    Sets DIO for Hi-Byte In, returns Hi-Byte SFX * 

in.dt.word             ( -- n )                           <dt>       dt2823.fth
    Sets DIO for 16-bit In, returns 16-bit word SFX * 

init.board             ( -- )                             <dspif>       dsp.fth
    Run DSP program to intialize board. SFX ** 

insidename?            ( word-nfa -- flag )               <tools>     tools.fth
    Does the Tstring occur inside name? 

install
    
into  <dsp>            debug.fth
    
inverse                ( -- )                             <con>     console.fth
    set inverse video 

is.def'd.to            ( acf of deferred word1 -- acf of  <tmp>       tmptr.fth
    * 
    where word1 is deferred to word2

isname                 ( n -- f )                         <dsp>       debug.fth
    f=-1: n appears to be a cfa. f=0: not, 
    f=1: n not in dictionary space (uses HERE).

itime                  ( n -- )                           <dsp>         run.fth
    Set integration time (ms) ** 
    NOTE: can't change during crun

lc                     ( "rest-of-line" -- )              <dsp>         run.fth
    Enter a local comment ** 

lc_clean               ( -- )                             <run>         run.fth
    Erase local comment 

linesthispage          ( n -- n )
    
listtype               ( "definer" -- )                   <tools>     tools.fth
    List all words of the given type * 

lmessage               ( -- )                             <fil>    ./fwheels/fi
    Print lambda error message 

loadclock              ( -- )                             <det>         det.fth
    load clock program onto dsp board SFX * 

loaddata               ( -- )                             <det>         det.fth
    load data acquisition pgm onto dsp boards SFX * 

loaddet                ( "filename" -- )                  <dsp>         det.fth
    loaddet filename SFX ** 

loadobjectfile         ( pstr -- )                        <dspif>       dsp.fth
    load .LOD file onto spectrum board SFX * 
    NOTE: loadobjectfile expects a
    null-terminated string

loadrundata            ( -- )                             <runrun>   runrun.fth
    Copy parameters to all boards SFX 

loadrundata?           ( -- )                             <partial> partial.fth
    if det present, load run data on spectrum SFX * 

loaduser               ( "name" -- )                      <dsp>        xdir.fth
    Load user's custom file. SFX ** 

lower                  ( ch -- ch )                       <misc>       misc.fth
    Convert character to lowercase 

ltime                  ( pstr -- )                        <fits>       fits.fth
    Get exact.time and store as time of scan end(last). 

make-data-ro           ( -- )                             <fits>       fits.fth
    make the last-written data file read-only SFX 

makedir                ( "dirname" -- )                   <xdir>       xdir.fth
    makedir dir.name with error checking SFX 

match.amp              ( ' \ADx -- )                      <tmp>       tmptr.fth
    Converts ADx to temp using ' ADx * 

matchesname?           ( word-nfa -- flag )               <tools>     tools.fth
    Does the Tstring match the name? 

matchestype?           ( word-nfa -- flag )               <tools>     tools.fth
    Does the Ttype match the type? 

millisec               ( n -- )                           <fil>       wheel.fth
    delay n milliseconds ** 

moderate               ( -- )                             <dsp>         nod.fth
    go to moderately fast clocking mode SFX ** 

move.fw                ( n -- )                           <fil>       wheel.fth
    shortest path move to fwp=n, with backlash SFX ** 

movel                  ( adr1 len adr2 maxwid -- )
    
mover                  ( adr1 len adr2 maxwid -- )
    
nasm-fp                ( -- )                             <dsp>          fp.fth
    Use the National Air & Space Museum's Fabry Perot. 

nave.ad0               ( n -- )                           <dsp>          fp.fth
    Set the number of samples of ad0 to take to 
    eliminate noise interference.

ncd                    ( n -- )                           <dsp>         run.fth
    Set number of co-add frames ** 
    NOTE: can't change during crun

ncol                   ( n -- )                           <dsp>         det.fth
    # cols in next image. Can't change during crun ** 

newline                ( -- )                             <fits>       fits.fth
    Clear line 

newscanline            ( -- )                             <scandir> scandir.fth
    Clear a line of 180 characters. 

nextobject             ( -- )                             <xdir>       xdir.fth
    advance file name to next number in sequence 

night                  ( "night" -- )                     <dsp>        xdir.fth
    night dir.name SFX ** 

nimage                 ( n -- )                           <dsp>      runrun.fth
    Sets the number of images you want to save in 
    one FITS file while in fast photometry mode.

nm                     ( lambda[nm] -- )                  <dsp>    ./fwheels/fi
    move to lambda SFX ** 

nm1                    ( lambda[nm] -- )                  <dsp>    ./fwheels/fi
    Setup CVF1. 

nm2                    ( lambda[nm] -- )                  <dsp>    ./fwheels/fi
    Setup CVF2. 

nml                    ( lambda[nm] -- )                  <dsp>    ./fwheels/fi
    Move to wavelength on long CVF. 

nms                    ( lambda[nm] -- )                  <dsp>    ./fwheels/fi
    Move to wavelength on short CVF. 

no.partials?           ( -- )                             <partial> partial.fth
    aborts if buffers have partial images 

nod                    ( -- )                             <dsp>         nod.fth
    nod the telescope SFX ** 
    [ <fil> ]

nod-delay              ( n -- )                           <dsp>         nod.fth
    the delay after nod, in seconds ** 

noise                  ( -- )                             <dsp>       extra.fth
    Measure detector noise SFX ** 

noobject               ( -- )                             <dsp>        xdir.fth
    clears object path and filename SFX ** 

normal                 ( -- )                             <con>     console.fth
    set normal video 

nout                   ( n -- )                           <dsp>         det.fth
    # inputs in next image. Can't change during crun ** 

nrow                   ( n -- )                           <dsp>         det.fth
    # rows in next image. Can't change during crun ** 

nsamp                  ( n -- )                           <dsp>         run.fth
    Set number of samples/level (level = s, r, or p) ** 
    NOTE: can't change during crun

nst>  <dsp>            debug.fth
    
nstack  <dsp>          debug.fth
    
nstep                  ( -- )                             <fil>       wheel.fth
    step filter wheel motor n steps. SFX ** 

nta                    ( n -- )                           <dsp>         run.fth
    Set number of throw-away frames ** 
    NOTE: can't change during crun

numcols                ( -- numcols )                     <red>         red.fth
    # cols in stats area 

numpix.rect            ( -- )                             <red>         red.fth
    # pixels in stats area 

numrows                ( -- numrows )                     <red>         red.fth
    # rows in stats area 

object                 ( "object" -- )                    <dsp>        xdir.fth
    make new objdir & start sequencing data files SFX ** 

objfile>objnum         ( -- n )                           <xdir>       xdir.fth
    Leave current object number on stack. 

objfilename            ( -- )                             <run>         run.fth
    Copy object file w/o path 

observer               ( "name" -- )                      <dsp>         run.fth
    Enter observer initials ** 

open-read              ( pstr -- fid | ABORT )            <misc>       misc.fth
    Open file for reading + err check SFX * 

open-scandir-append    ( -- )                             <scandir> scandir.fth
    Use a+ mode to write to scandir. Append 
    only allows writes to the end-of-file
    marker. If file doesn't exist, it is
    created. If file does exist, determine
    how many lines for current page so that
    header may be correctly written at top
    of page.

open-write             ( pstr - fid | ABORT )             <misc>       misc.fth
    Open file for writing + err check SFX * 
    and overwrite/backup/abort options *

out.dt.port0           ( n -- )                           <dt>       dt2823.fth
    Sets DIO for Low-Byte Out, Outputs Low-Byte SFX * 

out.dt.port1           ( n -- )                           <dt>       dt2823.fth
    Sets DIO for Hi-Byte Out, Outputs Hi-Byte SFX * 

out.dt.word            ( n -- )                           <dt>       dt2823.fth
    Sets DIO for 16-bit Out, Outputs 16-bit word SFX * 

overwrite-fits         ( filename databuffer #bytes -- )  <fits>       fits.fth
    Write Image File SFX * 
    If file exists -> over write it *

p.on.array?            ( n2 n1 -- )                       <partial> partial.fth
    aborts if new p1row + pnrow - 1 > nrow 

p1row                  ( n -- )                           <dsp>     partial.fth
    sets 1st row of array for partial im copy ** 

pbkg.patch             ( -- )                             <partial> partial.fth
    Add partial image count to bkg SFX 

pbrun                  ( -- )                             <dsp>     partial.fth
    prun into bkg buffer SFX ** 

pbscan                 ( -- )                             <dsp>     partial.fth
    bkg buf partial image, save to tmp SFX ** 

pbuf.full?             ( -- flag )                        <partial> partial.fth
    check for image buffer full 

pcount                 ( n -- )
    
pfocus                 ( -- )                             <dsp>     partial.fth
    Wait for <cr> between successive partial images SFX ** 

pget.data              ( -- )                             <partial> partial.fth
    get a partial image from spectrum memory SFX * 
    SHOULD: corrupt.hist at beginning; *
    raw.partialhist at end *

pix                    ( col row -- )                     <dsp>         red.fth
    Displays the pixel value ** 

pmax.count             ( -- n )                           <partial> partial.fth
    number of partial images that fill buf 

pnothing               ( -- )                             <dsp>     partial.fth
    No wait between successive partial images SFX ** 

pnrow                  ( n -- )                           <dsp>     partial.fth
    set number of rows per partial image copy ** 

poffset                ( -- n )                           <partial> partial.fth
    offset in bytes from start of buffer 

prev-objfile           ( -- pstr )                        <vf>           vf.fth
    Figure out what the previous objfile was. 

prim#>string           ( n -- adr len )
    
prims                  ( -- )                             <tools>     tools.fth
    List all primitives in the dictionary ** 

print.temp             ( n|flag2 flag -- )                <tmp>       tmptr.fth
    Type temp if flag=true * 
    else error msg

prun                   ( -- )                             <dsp>     partial.fth
    get partial images, do save to disk SFX ** 
    SHOULD define as : prun pscan savedata lc_clean ; **

psavedata              ( -- )                             <dsp>     partial.fth
    save a buffer filled with partial images SFX * 
    SHOULD only call saved/savedata, NOT savetmp *
    can create psavetmp to save a buffer tmp file *

pscan                  ( -- )                             <dsp>     partial.fth
    Get a partial image, save to tmp SFX ** 

psrc.patch             ( -- )                             <partial> partial.fth
    Add partial image count to src SFX 

psrun                  ( -- )                             <dsp>     partial.fth
    prun into src buffer SFX ** 

psscan                 ( -- )                             <dsp>     partial.fth
    sig buf partial image, save to tmp SFX ** 

pstrcon:               ( pstr "name" -- )                 <misc>       misc.fth
    define packed str constant SFX 

putcol                 ( adr len col -- )                 <fits>       fits.fth
    put unpacked str into line buffer @ col 

putcol-180             ( adr len col -- )                 <scandir> scandir.fth
    put unpacked str into line buffer @ col 

putline                ( fid addr len -- fid )            <misc>       misc.fth
    put line into file, see fits.fth SFX * 

putname                ( addr len -- )                    <scandir> scandir.fth
    Put an unpacked str representing the name 
    of the banner field into scanline.

putnum                 ( fid n -- fid )                   <misc>       misc.fth
    put number onto line in file;seefits.fth SFX * 

putnum                 ( n col wid -- )                   <fits>       fits.fth
    put # into line buffer @ col, right justify 

putnum-180             ( n col wid -- )                   <scandir> scandir.fth
    put # into line buffer @ col, right justify 

putr                   ( addr len col wid -- )
    
putr-180               ( addr len col wid -- )
    
putvalue               ( addr len -- )
    
query                  ( -- )
    
raw                    ( -- )                             <con>     console.fth
    Puts term in raw mode, may change tty settings SFX 

raw.hist               ( -- )                             <run>         run.fth
    Use after successful copy pix to databuffer 

raw.partialhist        ( -- )                             <partial> partial.fth
    set history to "raw partial data" 

rdblock16i             ( memtype addr # target step -- )  <dspif>       dsp.fth
    Copy block from dspboard SFX * 

readarray              ( -- )                             <dsp>     partial.fth
    copy parameters & verify, then read array SFX * 

recover                ( -- )                             <dsp>         run.fth
    load setup from last.run SFX ** 

rect                   ( col row -- )                     <dsp>         red.fth
    Rectangle statistics and display ** 
    Uses rectcols & rectrows for size **

rectcols               ( numcols -- )                     <dsp>         red.fth
    Set # of cols in stats rectangle ** 
    Must be between 1 and ncol **

rectrows               ( numrows -- )                     <dsp>         red.fth
    Set # of rows in stats rectangle ** 
    Must be between 1 and nrow **

removeflag             ( -- )                             <dspif>       dsp.fth
    Lower flag that dsp board reads. SFX * 

rename.bak             ( pstr -- )                        <misc>       misc.fth
    renames file 'pstr' with extension .BAK 

resume2  <dsp>         debug.fth
    
return                 ( -- )                             <dsp>         nod.fth
    Return to initial settings after a fast, SFX ** 
    moderate or slow.

rjustify               ( addr len field )                 <gen>    genwords.fth
    Display LEN characters starting at ADDR 
    Right justified in a field of FIELD chars.

rms                    ( col row -- )                     <dsp>         red.fth
    print statistics but not data ** 
    SHOULD: rename this (rect) & rect calls it **

rms.rect               (F: -- rms )                       <red>         red.fth
    root mean square for clipped rectangle onFloatStack 

row                    ( row -- )                         <dsp>         red.fth
    Row statistics and display ** 

rowrms                 ( col row -- )                     <dsp>       extra.fth
    Average the noise in several adjacent rows ** 

rprompt
    
run                    ( -- )                             <dsp>      runrun.fth
    get a complete image, save to disk as object.nnn SFX ** 

savea-                 ( -- )                             <dsp>        fits.fth
    After executing an a-, save sigbuf to disk ** 
    in a file called "aminus". This is similar
    to how sscan and bscan save their buffers
    (i.e. savetmp).

savedata               ( -- )                             <dsp>        fits.fth
    Swap bytes and then executes (savedata). SFX ** 

savedet                ( -- )                             <dsp>         det.fth
    saves detector data in file in DETNAME field SFX ** 
    NOTE: Parameter order here must match
    the order in "loaddet

savedetas              ( "newfilename" -- )               <dsp>         det.fth
    savedetas newfilename SFX ** 

saverun                ( -- )                             <dsp>         run.fth
    save setup under last.run SFX ** 

savesetup              ( "name" -- )                      <dsp>         run.fth
    save setup to file "name" SFX ** 

savetmp                ( -- )                             <dsp>        fits.fth
    Swaps bytes and then executes (savetmp). SFX ** 

scan                   ( -- )                             <dsp>      runrun.fth
    get a complete image, save diskfile named 4buffer SFX ** 

scandir                ( -- )                             <scandir> scandir.fth
    Write information about object just acquired. Only 
    use for runs. Execute before nextobject.

scandir-init           ( -- )                             <scandir> scandir.fth
    Open file to append, closing a previous file 
    if necessary.

sec                    ( n -- )                           <fil>       wheel.fth
    delay n seconds ** 

sec-obs                ( -- n )                           <fits>       fits.fth
    Convert TIME-OBS to seconds. 

seeall                 ( "name" -- )                      <dsp>       tools.fth
    Show definitions for words of given name ** 

send-to-gui            ( -- )                             <xshow>  xshowall.fth
    Executes forth-rpc "call" command to send 
    a string to the GUI.

send-to-vf             ( -- )
    
send.float             ( f1 n2 -- )                       <xshow>  xshowall.fth
    Send a floating point number to the GUI. 

send.number            ( n1 n2 -- )                       <xshow>  xshowall.fth
    Convert a variable (n1), and the 
    corresponding number (n2) which
    determines the function to call
    upon reaching the GUI, to a string
    and send the string to the GUI via RPC.

send.string            ( pstr n2 -- )                     <xshow>  xshowall.fth
    Create xsstring from n2 and pstr. 
    n2 is the number that tells the GUI
    which value is being sent.
    pstr is the info you wish to send to
    the GUI.

server                 ( offset -- )                      <rpc>         rpc.fth
    Exits when a key is typed 

set.col                ( -- 1 nrow )                      <red>         red.fth
    Sizes for 1 column 

set.cur                ( line col -- )                    <con>     console.fth
    set cursor to line 1-25, col 1-80 

set.d/a                ( adu n -- )                       <dt>       dt2823.fth
    D/A Conversion with v in A/D Units. SFX ** 
    If n==0 or 1, DAC v on channel n. Else error. **
    adu is clipped into the range [-32768, 32767] **

set.d/a.mv             ( v n -- )                         <dt>       dt2823.fth
    Same as SET.D/A but v is in tenths SFX ** 
    of Millivolts. v is clipped into **
    the range [-100000,100000]. **

set.dac.voltage        ( mV n -- n )                      <urfp>       urfp.fth
    Set the target voltage for the IR FP's 
    DAC.

set.dt.clock.100k      ( -- )                             <dt>       dt2823.fth
    Set freq of Pacer Clock to 100 kHz decimal SFX ** 

set.halves             ( numcols numrows -- )             <red>         red.fth
    Set halves given col & row sizes 

set.rect               ( -- rectcols rectrows )           <red>         red.fth
    user-specified Sizes for rectangle 

set.row                ( -- ncol 1 )                      <red>         red.fth
    Sizes for 1 row 

set.square             ( -- squareside squareside )       <red>         red.fth
    user-specified Sizes for square 

setdatapath            ( "name" -- )                      <dsp>        xdir.fth
    setdatapath dir.name SFX ** 

setdir                 ( "dirname" -- )                   <xdir>       xdir.fth
    setdir dir.name with error checking SFX 

setlinepos             ( n -- )                           <scandir> scandir.fth
    set linepos to the location of the next 
    position to write to in scanline.

setsoff                ( -- )                             <det>         det.fth
    prevent loading DSP files & setting voltages SFX 

setson                 ( -- )                             <det>         det.fth
    allow loading DSP files & setting voltages SFX 

setsquarepos \         ( xpos ypos square# -- )                       \ Sets th
        Options are 1, 2, 3 or 4

setup                  ( "name" -- )                      <dsp>         run.fth
    load run parameters from given file SFX ** 

setvbias               ( -- )                             <det>         det.fth
    Put bias volatage on D/A Channel 1. SFX * 

setvgate               ( -- )                             <det>         det.fth
    Put gate volatage on D/A Channel 0. SFX * 

shape                  ( -- )                             <red>         red.fth
    Display last statistical area's size & centroid ** 
    SHOULD rename .shape **

show.col               ( -- )                             <red>         red.fth
    Display pixel values for 1 col of stats area 

show.colnums           ( -- )                             <red>         red.fth
    Display column numbers for statistical area 

show.diodat            ( -- )                             <dt>       dt2823.fth
    Shows In/Out states and values of DIO bytes 

show.filename          ( -- )                             <run>         run.fth
    Display current buffer's filename 

show.history           ( -- )                             <run>         run.fth
    display the history buffer in the forth window 

show.rect              ( -- )                             <red>         red.fth
    Display pixel values for statistical rectangle 

show.row               ( -- )                             <red>         red.fth
    Display pixel values for 1 row of stats area 

showall                ( -- )                             <dsp>         run.fth
    show all parameters ** 

showdefinition         ( word-nfa -- )                    <tools>     tools.fth
    Show definition of word 

showdet                ( -- )                             <dsp>         det.fth
    Display current detector parameters ** 

showname               ( word-nfa -- )                    <tools>     tools.fth
    Show name of word 

showred                ( -- )                             <dsp>         red.fth
    Show values of data reduction parameters ** 

showrun                ( -- )                             <dsp>         run.fth
    update A/D values then show all non-det parameters ** 

siftdsp                ( "word" -- )                      <dsp>       tools.fth
    Sift only in <dsp> vocabulary. ** 

slow                   ( -- )                             <dsp>         nod.fth
    go to slowest, most sensitive, clocking mode SFX ** 

soundoff               ( -- )                             <dsp>        misc.fth
    do not sound bell (at end of each scan, etc.) ** 

soundon                ( -- )                             <dsp>        misc.fth
    sound bell (at end of each scan, etc.) ** 

sprompt
    
square                 ( col row -- )                     <dsp>         red.fth
    Square statistics and display ** 
    Uses squareside for size **

squareside             ( sidelen -- )                     <dsp>         red.fth
    Set # of rows & # of cols in stats square ** 
    Must be between 1 and min(ncol, nrow) **

src                    ( -- )                             <dsp>         run.fth
    Make src buffer the current image buffer SFX ** 

src.params             ( -- )                             <run>         run.fth
    select src file & history SFX 

srun                   ( -- )                             <dsp>      runrun.fth
    Select src buffer, then execute run SFX ** 

sscan                  ( -- )                             <dsp>      runrun.fth
    Select src buffer, then execute scan SFX ** 

start-rpc              ( offset -- )                      <rpc>         rpc.fth
    Start up rpc server process for specified 
    PROGNUM (88 + offset).

start.board            ( start.addr -- )                  <dspif>       dsp.fth
    Start NIR prog running on DSP board SFX ** 

start.burst            ( start.addr -- )                  <runrun>   runrun.fth
    Start clock board & databoards SFX 

start.crun             ( start.addr -- )                  <runrun>   runrun.fth
    Start databoards SFX 

stats                  ( -- )                             <red>         red.fth
    Display last statistical results ** 
    SHOULD rename .stats **

stdorder               ( -- )                             root     platform.fth
    put user in <dsp> vocabulary (= startup location) SFX ** 
    by setting standard context and current (order) **

step                   ( -- )                             <fil>       wheel.fth
    step motor in dir given by the direction-bit SFX ** 

stop.board             ( -- )                             <dspif>       dsp.fth
    Stop NIR program running on dsp 56001 board SFX ** 

stopdsp                ( -- n )                           <runrun>   runrun.fth
    stops current board and return error codes SFX 

store,t.inc.v          ( -- )                             <tmp>       tmptr.fth
    Store truth value of "T increases w/ increasing V" 

store.filename         ( -- )                             <run>         run.fth
    Store filename for current buffer 

storemax,mins          ( -- )                             <tmp>       tmptr.fth
    stores max,min values for Temp and Voltage 

strpad  <dsp>          debug.fth
    
syscalls               ( -- )                             <tools>     tools.fth
    List all syscalls in the dictionary ** 

t,                     ( n -- )                           <tmp>       tmptr.fth
    Store in ts.tcurv at index 

t@
    
talarm                 ( n -- )                           <dsp>       tmptr.fth
    Set tmp(K) to signal when it is getting too high. 

tcheck                 ( -- )                             <tmp>       tmptr.fth
    Check to see if fanout tmp is getting too warm. 

tdelta                 ( n -- )                           <dsp>       tmptr.fth
    Range around talarm for which no alarm is sounded. 

telescope              ( "name" -- )                      <dsp>         run.fth
    Enter telescope name ** 

time                   ( -- )                             <dsp>       tools.fth
    Print current time. SFX ** 

timestamp              ( -- )                             <dsp>      runrun.fth
    First pixel is seconds since units of .01 seconds. 
    Second pixel is fanout tmp, units of .1 degrees kelvin.

tmps                   ( -- )                             <dsp>       tmptr.fth
    print out temperatures and time SFX ** 

tomid
    
true!                  ( addr -- )                        <gen>    genwords.fth
    Stores true at ADDR. Used where DRO used 1set 
    to store TRUE (= FALSE NOT)

ts.calcmv              ( t*10 top-bp# bottom-bp# -- mV*10 <tmp>       tmptr.fth
    same as calctemp, * 
    but for volts not t *

ts.calctemp            ( mV*10 top-bp# bottom-bp# -- t*10 <tmp>       tmptr.fth
    calculates * 
    temperature via linear regression between nextbp# and *
    nextbp#-1 (i.e. prev bp#)

ts.mv>t                ( v -- n|flag2 flag )              <tmp>       tmptr.fth
    convert mv to ts temperature * 
    <n, true> iff in range 1.4-380 k
    <false, false> iff above 380 k
    <true, false> iff below 1.4 k

ts.table               ( -- )                             <tmp>       tmptr.fth
    prints out ts voltage-temperature table ** 

ts.tmp                 ( temp[ts]|flag2 flag -- )         <tmp>       tmptr.fth
    Print a TS temperature. * 

ts>decimalstr          ( temp[ts]|flag2 flag -- addr len  <xshow>  xshowall.fth
    Print a TS temperature. * 

type.r                 ( addr count width -- )            <misc>       misc.fth
    type right justified 

up                     ( -- )                             <fil>       wheel.fth
    prepare to go up steps. Set the direction bit to 0. SFX ** 

update.gui.a/d         ( -- )                             <xshow>  xshowall.fth
    Send the a/d temperatures to the GUI 
    for updating. Unit conversion should
    be handled by the GUI.

update.gui.text        ( -- )                             <xshow>  xshowall.fth
    Update the text fields on the GUI. 

updategui              ( -- )                             <dsp>    xshowall.fth
    Initialize all GUI elements. SFX ** 

upper                  ( ch -- ch )                       <misc>       misc.fth
    Convert character to uppercase 

urir-fp                ( -- )                             <dsp>          fp.fth
    Use the URIR Fabry Perot. 

v,                     ( n -- )                           <tmp>       tmptr.fth
    Store in ts.vcurv at index and increment n. 

valid.p1row?           ( n -- )                           <partial> partial.fth
    aborts if invalid pnrow 

valid.pnrow?           ( n -- )                           <partial> partial.fth
    aborts if invalid pnrow 

vars                   ( -- )                             <tools>     tools.fth
    List all variables in the dictionary ** 

vbias                  ( n -- )                           <dsp>         det.fth
    Bias voltage. N in millivolts. Calls setvbias SFX ** 

version                ( -- )                             <dsp>       tools.fth
    Display version number of dspsys being used. ** 

vf-active              ( "string" -- )                    <dsp>          vf.fth
    Make a canvas active (a, b, c, d, e) SFX ** 

vf-buffer              ( "string" -- )                    <dsp>          vf.fth
    Changes the buffer for the active canvas. SFX ** 

vf-dofile              ( "string" -- )                    <dsp>          vf.fth
    Execute a VF macro. SFX ** 

vf-init                ( -- )                             <dsp>          vf.fth
    Setup vf for use with new object. 

vf-load-bkg
    
vf-load-brun
    
vf-load-src            ( -- )                             <vf>           vf.fth
    Load the current src file into the appropriate 
    buffer.

vf-load-srun           ( -- )                             <vf>           vf.fth
    Load the last image into a src buffer on VF. 

vf-path                ( "string" -- )                    <dsp>          vf.fth
    Set the datapath for VF to "string". SFX ** 

vf-read                ( bufname filename -- )            <dsp>          vf.fth
    Cause VF to read a specific file ** 
    into a specific buffer.

vf-src-bkg             ( -- )                             <vf>           vf.fth
    Subtract bkg buffer from src buffer and place 
    in src buffer.

vfcmd                  ( "string" -- )                    <dsp>          vf.fth
    Read a user inputed string and send the ** 
    command to VF to be executed. The command
    given must be acceptable by the command
    prompt in VF. A list of commands can be
    found in Appendix A of the VF documentation.

vgate                  ( n -- )                           <dsp>         det.fth
    Gate voltage. N in millivolts. Calls setvgate SFX ** 

vname xname ;  <dsp>   debug.fth
    
vnm  <dsp>             debug.fth
    
vocs                   ( -- )                             <tools>     tools.fth
    List all vocabularies in the dictionary ** 

vocsearch              ( voc-cfa -- )                     <tools>     tools.fth
    Loop through all words in vocab 
    when Tcondition? is true, execute Taction

vocsifting             ( "pattern" -- )                  <dsp>        tools.fth
    List all words containing pattern ** 

voff                   ( n -- )                           <dsp>         det.fth
    Clock voltage - required to turn off (NO FX EVER) ** 

von                    ( n -- )                           <dsp>         det.fth
    Clock voltage - required to turn on (NO FX EVER) ** 

wait.for.muxbusy.clear ( -- )                             <dt>       dt2823.fth
    7. Auxilliary routine SFX 

wait.til.read.done     ( -- )                             <partial> partial.fth
    wait til programs done or user aborts SFX * 

waitforkey             ( pstr -- key )                    <misc>       misc.fth
    wait for key in pstr (LOWER CASE!) 

whatsnew               ( -- )                             <dsp>       tools.fth
    Display specific version info, ** 
    i.e. major changes in operation.

whatvoc                ( "name" -- )                      <dsp>       tools.fth
    List all words with the given name ** 

wlsigned               ( w -- l )                         <dsp>       debug.fth
    Convert signed word to signed longword. 
    Added by kevin from zfortxm.lib

wrblock24              ( memtype addr count sourceaddr -- <dspif>       dsp.fth
    Copy block to dspboard SFX * 

write-64k              ( addr len fd -- )                 <fits>       fits.fth
    Front end to fputs. Prints 65k blocks. 

write-fits             ( filename databuffer #bytes -- )  <fits>       fits.fth
    Write FITS Image File SFX * 
    If file exists -> ask the user *

write-scandir-banner   ( -- )                             <scandir> scandir.fth
    Write the banner information for 
    current object.

write-scandir-body     ( -- )                             <scandir> scandir.fth
    Write data for current scan. 

write-scandir-comments ( -- )                             <scandir> scandir.fth
    If comment has changed or is the first 
    comment to be written for this object
    since starting dspsys, write it.

write-scandir-header   ( -- )                             <scandir> scandir.fth
    Write the header for column definitions. 

writescan              ( -- )                             <scandir> scandir.fth
    Write line180 to a file. 

ws.a/d>temp            ( a/d[ws] -- temp[ws] flag )       <tmp>       tmptr.fth
    Calculate WS temp from A/D * 

ws.correct             ( mV*10 -- mV*10 )                 <tmp>       tmptr.fth
    corrects ws voltage for buffer * 
    amplifier gain and offset

x
    
x ." xyz" ; ' x >body @
    
x 123456 ; ' x >body @
    
x ; ' x >body @ forget
    
x >r ; ' x >body @ forg
    
x ?do loop ; ' x >body
    
x [""] xyz ; ' x >body
    
x abort" " ; ' x >body
    
x case of endof endcase
    
x create does> ;
    
x do +loop ; ' x >body    \ ' branch constant $+loop
    
x do loop ; ' x >body /   \ ' branch constant $loop
    
x do loop ; ' x >body @
    
x i ; ' x >body @ forge
    
x if else then ; ' x >b   \ ' branch constant $else
    
x if then ; ' x >body @
    
x j ; ' x >body @ forge   \ : x i2 ; ' x >body @ forget x
    
x leave ; ' x >body @ f
    
x r> ; ' x >body @ forg
    
x skipstr ; ' x >body @
    
xhost                  ( "name" -- )                      <dsp>         rpc.fth
    Set rpchost to the name of the RPC server. SFX ** 

xname  <dsp>           debug.fth
    
xshowall               ( -- )                             <dsp>    xshowall.fth
    Tell FORTH to send update info to Xshowall GUI. ** 
    Initially, these are all set to noop.

xshowall.ad0name
    
xshowall.ad1name
    
xshowall.ad2name
    
xshowall.ad3name
    
xshowall.adctime
    
xshowall.adname
    
xshowall.bandwidth
    
xshowall.bgsub
    
xshowall.bkg
    
xshowall.clockpgm
    
xshowall.comment0
    
xshowall.comment1
    
xshowall.comment2
    
xshowall.comment_clean
    
xshowall.ctstime
    
xshowall.datapgm
    
xshowall.datastate
    
xshowall.detname
    
xshowall.display
    
xshowall.fastphot
    
xshowall.filterwl
    
xshowall.fwn
    
xshowall.fwp
    
xshowall.gc
    
xshowall.gc_clean
    
xshowall.itime
    
xshowall.lc
    
xshowall.lc_clean
    
xshowall.ncd
    
xshowall.ncol
    
xshowall.night
    
xshowall.nimage
    
xshowall.nout
    
xshowall.nrow
    
xshowall.nsamp
    
xshowall.nta
    
xshowall.object
    
xshowall.observer
    
xshowall.runmode
    
xshowall.sampmode
    
xshowall.src
    
xshowall.telescope
    
xshowall.updatebuffer
    
xshowall.vbias
    
xshowall.vgate
    
xshowall.voff
    
xshowall.von
    
xshowall?              ( -- flag )                        <xshow>  xshowall.fth
    Is xshowall mode on?